## Slide 1: From 31.5 billion readings to one decision
SMART-FACTORY DATA PLATFORM
How factory data should flow, what we built and measured on real Bosch data, and the live system
100
CNC machines
3
plants: Chakan · Oragadam · Manesar
876,100
machine-hours in SQL
Live
on Google BigQuery
Tirthanker Singh · github.com/TirthankerSingh/industrial-data-platform · industrial-data-platform.streamlit.app
Notes: We didn't just compare clouds on paper. We built the pipeline, measured it on real factory data, and the last slide is the live system.

## Slide 2: Nine stages, one command to rebuild, one source of truth
WHAT WE BUILT
01
Collect 4 datasets
02
Edge features
03
Calibrate
04
Fleet table
05
PostgreSQL / BigQuery
06
ML models
07
MQTT gateway
08
Dashboard
09
Decision
1
command rebuilds everything
0
numbers typed by hand
4
public datasets, each labelled
Notes: Raw datasets go in on the left, a manufacturing decision comes out on the right. Every number in the report, slides and dashboard comes from these same scripts, so nothing is typed in by hand.

## Slide 3: Pipeline design moves the bill more than the cloud does
PIPELINE COMPARISON 1
Chart: Monthly cloud cost, ₹ lakh (same factory, same data)
| S0 one message per reading | S3 raw 2 kHz streamed | S1 batched raw | S2 batched + edge features
Azure | 14.26 | 3.94 | 0.8 | 0.8
AWS | 29.92 | 2.85 | 0.43 | 0.43
18–70×
lower monthly bill when the edge batches messages instead of sending one per reading
₹14–30 lakh → ₹43–80k a month
Batching at the edge is the single biggest cost lever, bigger than which cloud you pick.
Notes: Same factory, same data: 14 to 30 lakh rupees a month if every reading is its own message, 43 to 80 thousand if the edge batches. Batching at the edge is the single biggest lever, bigger than which cloud you pick. Prices from official calculators, FX 94.71 per USD, 21 Oct 2026.

## Slide 4: Compression gives 5×. Feature extraction gives 143×
PIPELINE COMPARISON 2
5×
lossless compression of raw Bosch vibration (Parquet + Zstd): noise doesn't compress
143×
smaller with 42 edge features a second instead of 6,000 raw samples
0.98
ROC-AUC: the fault signal survives, good vs bad operations
Measured on real Bosch production data: 1,702 operations, 2 kHz × 3 axes
Notes: This is measured on real Bosch production data, not assumed. You can't compress noise, but you can summarise it: RMS, kurtosis, crest factor, band energies. 143 times smaller and the anomaly model still separates good from bad at 0.98.

## Slide 5: Three shapes of data need three kinds of home
STORAGE COMPARISON
 | Data lake | Data warehouse | Lakehouse
Holds | Everything, raw | Clean tables | Everything + clean tables
Structure | Decided when reading | Fixed before loading | Both
Cost | Lowest | Highest | Low
Updates, de-dup, history | No | Yes | Yes
Examples | S3, ADLS, GCS | Snowflake, BigQuery, Redshift | Databricks, Fabric
Our data | Raw vibration | Fleet table, KPIs | All of it, one copy
99%+
of the bytes are raw vibration, the data that needs the least SQL
→ that one fact picks a lakehouse
Notes: A lake is cheap but messy, a warehouse is tidy but costly for raw signals. A lakehouse is the storeroom with a librarian: cheap open files plus a transaction log for de-duplication, updates and history. Over 99% of our bytes are raw vibration, the data that needs the least SQL. That one fact chooses the storage design.

## Slide 6: Everyone is converging on the lakehouse
PLATFORM COMPARISON
Lakes
Amazon S3 · Azure ADLS · Google Cloud Storage
Cheap, durable home for raw signals and files
Warehouses
Snowflake · Google BigQuery · Amazon Redshift
Best SQL and reporting; awkward for raw signals and heavy ML
WE USED: BigQuery
Lakehouses
Databricks (Delta Lake) · Microsoft Fabric
Open formats, ACID, one copy for BI and ML
OUR RECOMMENDATION
Operational DB
PostgreSQL
Strict rules, fast lookups for the app and KPIs
WE USED: PostgreSQL 16
65%
of enterprises already run most of their analytics on a lakehouse
42% of them moved from a cloud warehouse
Dremio, State of the Data Lakehouse 2024 (vendor-sponsored survey, n = 500)
Notes: Lakes store, warehouses query, lakehouses do both. Warehouses are adding lake features and lakehouses are adding warehouse features: they meet in the middle. We used two of these for real: PostgreSQL locally and Google BigQuery in the cloud. You'll see BigQuery live in the demo.

## Slide 7: Four public datasets, each with a job
OUR DATA
REAL
Bosch CNC
1,702 operations · 2 kHz × 3 axes · 2019–2021
JOB
Edge proof and anomaly detection
REAL
UMich CNC mill
18 experiments · spindle current · inspection
JOB
Spindle load, tool wear, quality
BENCHMARK
Microsoft Azure PdM
100 machines × 1 year · 876,100 hours
JOB
Fleet backbone, failure warning
BENCHMARK
AI4I 2020
10,000 records · 5 failure types
JOB
Machine physics, failure modes
Honesty rule: every calculated column is tagged DERIVED and traced back to its source in a provenance file.
Notes: Two real industrial datasets and two benchmarks. Bosch is the heart: real production vibration. Our rule was that no number appears without a source you can trace.

## Slide 8: 31.5 billion readings a year, before vibration
PART A · DATA VOLUME
1,000
per second
3.6 M
per hour
86.4 M
per day
2.59 B
per month
31.5 B
per year
100 machines × 10 sensors × 1 Hz
3.15 B
a year from ONE 100 Hz vibration sensor on one machine
10×
the whole 1 Hz fleet, if every machine gets one (315 B a year)
378 TB
a year of raw vibration at the real Bosch rate (96 Mbps)
Notes: 1 Hz fleet: 1,000 a second, 3.6 million an hour, 86.4 million a day, 2.59 billion a month, 31.5 billion a year. One 100 Hz sensor is 3.15 billion a year per machine; on every machine it is ten times the whole fleet. One vibration sensor outweighs everything else combined. That's why the edge exists.

## Slide 9: Many IIoT services in older comparisons are now retired
PART B · CLOUD COMPARISON
GCP IoT Core
retired 2023
Azure Time Series Insights
retired 2024
AWS IoT Analytics
end of support 2025
AWS IoT Events
retired 2026
AWS
STRENGTH
Best-documented edge buffering (Greengrass, SiteWise Edge) and SageMaker
GAP
IIoT stack is now separate parts after retirements
Microsoft Azure
STRENGTH
Most complete OPC UA → dashboard chain: IoT Operations, Fabric, Power BI
GAP
Highest cost, Kubernetes at the edge
Google Cloud
STRENGTH
Strongest, cheapest analytics: BigQuery, Vertex AI
GAP
No first-party factory-floor layer; partner edge needed
Notes: We checked every service against official vendor pages on 21 October 2026. A comparison built from old blog posts would recommend products that no longer exist. Full 13-criterion table is in the backup slides and the report.

## Slide 10: Azure 4.22 · AWS 3.92 · GCP 3.57
PART C · WEIGHTED DECISION MATRIX
Chart: Weighted score out of 5 (10 criteria)
| Azure | AWS | GCP
Weighted score | 4.22 | 3.92 | 3.57
Heaviest weights: Industrial IoT 15% · Cost 13% · Edge 12% · Security 12%
100%
of ±5-point weight shifts won by Azure
88.7%
of 10,000 random re-weightings won by Azure
≥ 35%
cost weight needed before AWS wins
WHY AZURE, FOR THIS FACTORY
Old Fanuc / Siemens controllers speak OPC UA
Microsoft tools already in the plants
Pune region next to Chakan
Edge design removes its cost and offline weaknesses
Notes: The score isn't the argument; the scenario is. Old OPC UA controllers, Microsoft tools already in the plants, and a Pune region next to Chakan. Azure wins every 5-point weight shift and 88.7% of 10,000 random re-weightings. AWS only wins if cost carries at least 35% of the weight.

## Slide 11: Every Azure block has a working stand-in in our prototype
PART F · ARCHITECTURE
Block | Azure (recommended) | Our prototype
CNC / sensors → protocol | OPC UA + MQTT | MQTT, ISA-95 topic tree
Edge gateway | IoT Operations, 7-day buffer | Python gateway, store-and-forward
Ingestion | IoT Hub / Event Hubs | MQTT broker → loader
Lake / time-series | ADLS lakehouse + Eventhouse | Parquet, bronze / silver / gold
SQL database | Azure Database for PostgreSQL | PostgreSQL 16 + Google BigQuery
Analytics / AI | Azure ML / Fabric | scikit-learn models
Dashboard → decision | Power BI | Streamlit, live
Open formats everywhere: the same data moved to BigQuery with identical query results.
Notes: Map of the professor's flow onto Azure services, and next to it what actually runs in our prototype. Open formats everywhere: that's why we could move the same data to BigQuery in under an hour without changing a single query result.

## Slide 12: We cut the internet. 0 of 482 messages lost
PART G · EDGE VS CLOUD
AT THE EDGE
2 kHz vibration → features
Immediate alarms, machine protection
Noise filtering, aggregation
Store-and-forward buffering
IN THE CLOUD
Fleet-level and historical analysis
Long-term lakehouse storage
ML training and management
Dashboards, remote access
0 / 482
messages lost when we stopped the receiver, then cut the link. 0 duplicates.
Latency
ms protection
Reliability
survives outages
Bandwidth
143× less
Cost
lakhs → thousands
Security
outbound only, IEC 62443
Scale
one node per plant
Notes: Protection needs milliseconds, plants lose internet, raw signals cost lakhs. So high-frequency work stays at the edge, and fleet-scale work goes to the cloud. We stopped the receiver, then cut the link, and all 482 messages arrived exactly once.

## Slide 13: 876,100 machine-hours, same answers on two engines
PART D · SQL
Question | Answer
Most parts produced | P3-TURN-05 · 199,677
Highest rejection rate | P2-GRIND-06 · 1.97%
Longest continuous run | P1-HMC-18 · 209 h
Highest average vibration | P1-VMC-13 · 1.86 mm/s (ISO zone B)
Parts on 16 Jun 2025 | 23,974 (381 rejected)
Fleet OEE | 75.3% (world-class 85%)
PostgreSQL 16 (local)
=
BigQuery (Mumbai)
Notes: One star schema: the machine_data fact table with machine, plant, part and alarm masters, and check constraints that reject impossible values. All 8 required questions answered. We ran the same SQL on BigQuery and got the same answers: that's our proof of no lock-in.

## Slide 14: Descriptive → diagnostic → predictive → prescriptive
ANALYTICS AND ML
Descriptive
What happened?
KPIs, OEE 75.3%, reject rates
Diagnostic
Why?
Alarm Pareto, ISO 10816 vibration zones
Predictive
What next?
Bosch anomaly ROC-AUC 0.98 (2019 → 2021), 24 h failure warning
Prescriptive
What to do?
Tool change on condition: rejects 1.50% → 0.92%
₹5.8 cr
estimated value a year (indicative)
We report precision too: one industry study found a 10% false-alarm rate wiped out the savings.
Notes: We climb all four rungs. The Bosch anomaly model holds when trained on 2019 and tested on 2021. We report precision as well as recall, because one industry study found a 10% false-alarm rate wiped out the savings of predictive maintenance.

## Slide 15: Downtime is expensive, and most factory data goes unused
WHY IT MATTERS
$2.3 M
per hour of downtime on an automotive line (Siemens, 2024)
11%
of revenue lost to unplanned downtime by the 500 largest industrial firms
80%
of industrial data is never used (ABB; WEF 2026)
Predictive maintenance typically cuts downtime 30–50% in mature programmes.
WHAT WE'RE HONEST ABOUT
Fleet backbone is simulated, and labelled as such
Worn-tool model doesn't generalise across only 18 experiments
Cloud runs on a BigQuery sandbox, not production Azure
Notes: Downtime costs the biggest industrial companies 11% of revenue, up to 2.3 million dollars an hour in automotive, yet most factory data is never used. We'd rather show you where our work breaks than hide it.

## Slide 16: From BigQuery to the live dashboard
LIVE DEMO
Google BigQuery
asia-south1
→
Service account
read-only
→
Streamlit dashboard
8 pages
1
Fleet overview: sidebar says “Google BigQuery”
2
Plant drill-down: one plant's heat map
3
Machine health: ISO 10816 zones
4
Alarms: top 4 types ≈ 80%
5
Edge demo: real Bosch waveform → 42 features
6
Data volume & cost: switch off batching, watch ₹ jump
7
Predictive maintenance: which machine first
industrial-data-platform.streamlit.app
Notes: Open the app 10 minutes early: the first load after sleep takes about 20 seconds. Path: 1 Fleet overview, point at the sidebar 'Data source: Google BigQuery', 83 of 100 running, OEE 75.5%. 2 Plant drill-down. 3 Machine health with ISO zones. 4 Alarms Pareto. 5 Edge demo: 'this is the 143x'. 6 Data volume and cost: turn off batching and watch the rupees jump. 7 Predictive maintenance ranking. Optional 30 s: BigQuery console query returns P3-TURN-05 = 199,677, same as PostgreSQL. Backup: screenshots in the hidden slides if Wi-Fi fails.

## Slide 17: Pipeline compared. Platforms compared. Decision made. Running live.
THANK YOU
Questions?
github.com/TirthankerSingh/industrial-data-platform · industrial-data-platform.streamlit.app
Notes: Pipeline compared, platforms compared, decision made, and it's running. Thank you.

## Slide 18: Cloud comparison across all 13 criteria
BACKUP B1 · PART B
Criterion | AWS | Microsoft Azure | Google Cloud
Industrial IoT | SiteWise Edge (OPC UA); several retired | IoT Operations: OPC UA, asset discovery | No first-party; partner (Litmus)
Ingestion | IoT Core, Kinesis | IoT Hub, Event Hubs, Eventstreams | Pub/Sub
Storage | S3, Timestream | ADLS Gen2, Eventhouse | Cloud Storage, BigQuery, Bigtable
Stream processing | Kinesis, Flink | Eventstreams (no-code) | Dataflow (code-first)
SQL | RDS / Aurora PostgreSQL | Azure DB for PostgreSQL | Cloud SQL, BigQuery
Analytics | Athena, QuickSight | KQL, Fabric, Power BI | BigQuery
AI/ML | SageMaker | Azure ML, Fabric | Vertex AI, BigQuery ML
Edge | Greengrass (best buffering docs) | IoT Operations on Arc | Partner edge only
Security | X.509, Mumbai region | OT PKI, Defender for IoT | India-pinned storage
Scalability | Very high | Very high | Very high
Integration | SAP via AppFlow | M365, Entra, Power BI, SAP | Best SAP connector
Ease of use | Separate parts | Fabric SaaS, common skills | BigQuery simple; edge DIY
Cost (edge design) | ₹43k / month | ₹80k / month | ₹33k / month
Notes: Full Part B table, checked against official sources on 21 October 2026.

## Slide 19: Monthly cloud cost in INR by pipeline design
BACKUP B2 · COST MODEL
Pipeline design | AWS | Azure | GCP
S0 one message per reading | ₹29,91,825 | ₹14,25,721 | ₹55,447
S1 batched raw 1 Hz + 100 Hz | ₹43,297 | ₹80,226 | ₹33,216
S2 batched + edge features | ₹43,121 | ₹80,085 | ₹32,928
S3 raw 2 kHz tri-axial | ₹2,84,788 | ₹3,94,487 | ₹1,19,208
FX ₹94.7145 per USD (RBI, 21 Oct 2026)
List prices from official pricing pages; India regions
Excludes edge hardware and people
Notes: Indicative list-price model; see docs/results/part_c_cost_model.csv.

## Slide 20: OT network zones and conduits (IEC 62443)
BACKUP B3 · SECURITY
Notes: Machines never accept inbound connections; the edge gateway makes outbound, encrypted connections only.