## Slide 1: How much data, and what it costs
PART A + PART C · DATA VOLUME AND CLOUD COST
Every number counted, sized and priced step by step: 100 CNC machines, 3 plants, 24×7
31.5 B
readings a year (slow sensors)
378 TB
a year if raw vibration went to cloud
143×
smaller after edge features
₹33–80k
a month for our design
Notes: I'll answer two questions: how much data the factory makes, and what it costs to move and keep it in the cloud. Every number on these slides is calculated in front of you, and the method is always the same: count, size, price, decide.

## Slide 2: Four steps, the same every time
THE METHOD
1 · Count
readings per second × seconds in the period
31.5 billion a year
2 · Size
readings × bytes per reading → bandwidth and storage
0.16 Mbps · 0.63 TB/yr
3 · Price
messages, bytes, GB stored, server hours × cloud list price
₹33k–80k a month
4 · Decide
cost is 1 of 10 weighted criteria
Azure 4.22 / AWS 3.92 / GCP 3.57
Conventions: month = 30 days = 2,592,000 s = 720 h · year = 365 days = 31,536,000 s · 1 USD = ₹94.7145 (RBI/FBIL, 21 Oct 2026) · public list prices
Notes: Count the readings, give each one a size in bytes, multiply by the cloud's price per message, per GB or per hour, and finally put cost into a weighted decision with nine other criteria. Conventions are the assignment's: a 30-day month and a 365-day year. Prices are public list prices converted at the RBI reference rate.

## Slide 3: 1,000 readings a second become 31.5 billion a year
STEP 1 · COUNT
100 machines × 10 sensors × 1 reading/s = 1,000 readings every second
Period | Seconds | Calculation | Readings
per second | 1 | 1,000 × 1 | 1,000
per hour | 3,600 | 1,000 × 3,600 | 3.6 million
per day | 86,400 | 1,000 × 86,400 | 86.4 million
per month (30 d) | 2,592,000 | 1,000 × 2,592,000 | 2.59 billion
per year (365 d) | 31,536,000 | 1,000 × 31,536,000 | 31.5 billion
Notes: Machines times sensors times rate gives a thousand readings a second. Every other period is that thousand multiplied by the seconds in it: 3.6 million an hour, 86.4 million a day, 2.59 billion a month, 31.5 billion a year. And these are only the slow sensors.

## Slide 4: One vibration sensor outweighs ten whole machines
STEP 1 · THE SHOCK NUMBER
3.15 B
readings a year from ONE 100 Hz sensor on ONE machine (100 × 31,536,000)
10×
all 10 slow sensors of that machine; on all 100 machines: 315 B a year
18.9 T
a year at the real Bosch rate: 100 machines × 3 axes × 2,000 Hz = 600,000/s
Why so fast? The Nyquist rule
To see a vibration at frequency f you must sample at least 2 × f. Bearing and tool faults appear between 100 Hz and several kHz, so vibration sensors need kHz sampling. Slow sampling simply misses the fault.
Notes: One 100 Hz sensor on one machine produces 3.15 billion readings a year, ten times all its slow sensors. Real accelerometers sample at 2 kHz on 3 axes, 600,000 readings a second for the fleet, 18.9 trillion a year. They have to be that fast because of Nyquist: to see a 500 Hz bearing fault you need at least 1,000 samples a second.

## Slide 5: From readings to bandwidth and storage
STEP 2 · SIZE
Field | Bytes
Timestamp (int64) | 8
Value (float64) | 8
Machine ID (int16) | 2
Sensor ID (int16) | 2
One reading | 20 B
bytes/s = readings/s × 20 B
Mbps = bytes/s × 8 ÷ 1,000,000
storage = bytes/s × seconds (86,400 a day, 31,536,000 a year)
Scenario | Readings/s | Bandwidth | Per day | Per year
Slow fleet, 1 Hz | 1,000 | 0.16 Mbps | 1.73 GB | 0.63 TB
Design point (1 Hz + 100 Hz) | 11,000 | 1.76 Mbps | 19 GB | 6.94 TB
Raw 2 kHz × 3 axes | 600,000 | 96 Mbps | 1,037 GB | 378 TB
96 Mbps = a plant's entire 50–100 Mbps internet line, 24 hours a day, before anyone sends an email.
Notes: A reading is not just a number: it needs a timestamp and the machine and sensor it came from. 20 bytes. Three formulas: bytes per second, times 8 for bits, times seconds for storage. Slow fleet: 1,000 × 20 = 20,000 bytes a second, 0.16 Mbps, 0.63 TB a year. Raw vibration: 600,000 × 20 = 12 MB a second, 96 Mbps, 378 TB a year. That is a plant's whole internet line.

## Slide 6: How you write it matters as much as how fast you sample
STEP 2 · ENCODING
Message type (measured) | Payload | Bytes per reading on the wire
JSON, one reading per MQTT message | 125 B | 219 B (payload + topic + header + TCP/IP)
JSON, 10 sensors batched per second | 296 B | 38 B
JSON, 100 Hz one-second block | 729 B | 8.25 B
Scenario | Binary 20 B | JSON one per message | JSON batched
Slow fleet, 1 Hz | 0.16 Mbps | 1.75 Mbps (11×) | 0.30 Mbps
Design point | 1.76 Mbps | 19.3 Mbps | 0.96 Mbps
Raw 2 kHz × 3 axes | 96 Mbps | 1,051 Mbps | 39.6 Mbps
Batching = the edge gateway packs a machine's readings for one second into one MQTT message.
Notes: We measured real message sizes. One reading in JSON is 125 bytes, 219 on the wire, eleven times the binary record, because names repeat in every message. Batching shares that overhead: 38 bytes a reading for ten sensors, 8 for a vibration block. And batching matters even more for money, as we'll see.

## Slide 7: Compression helps storage, but noise does not compress
STEP 2 · COMPRESSION (MEASURED ON REAL DATA)
Format | UMich CNC 10 Hz (REAL) | Bosch 2 kHz vibration (REAL) | Azure PdM hourly (BENCHMARK)
CSV (baseline) | 1.0× | 1.0× | 1.0×
CSV + gzip | 4.7× | 4.1× | 2.4×
Parquet + Snappy | 5.8× | 3.3× | 2.5×
Parquet + Zstd | 6.9× | 5.0× | 2.7×
6.9×
slow machine signals: smooth, repetitive values compress well
5.0×
raw vibration: mostly broadband noise, little pattern to remove
2.7×
already-averaged data: redundancy already gone
Notes: We didn't assume compression; we wrote three real datasets in six formats and measured. Parquet with Zstd gives 6.9 times on machine signals but only 5 on vibration, because vibration is noise and lossless compression can't remove noise. So compression can't solve the vibration problem. Feature extraction can.

## Slide 8: Send 42 numbers a second, not 6,000
STEP 2 · EDGE FEATURE EXTRACTION
24,000 B
raw per machine-second: 6,000 values × 4 B
168 B
42 features × 4 B (14 per axis × 3)
143×
smaller; 120× measured on all 1,702 Bosch files
Per axis: mean, RMS, peak, peak-to-peak, crest factor, kurtosis, skewness, 5 FFT band energies, dominant frequency, spectral centroid
378 TB → ~0.4 TB
a year in the lake for our design (860 B/machine-s, Parquet 6.9×)
0.69 Mbps
fleet uplink, about 1 % of a plant's line
ROC-AUC 0.98
fault signal kept: anomaly model on features
Notes: The edge gateway turns each second of 6,000 raw values into 42 features: RMS, kurtosis, frequency bands. 24,000 bytes become 168, 143 times smaller, and we measured 120 times on the full real dataset in 40 seconds on a laptop. The fault signal survives: AUC 0.98. Our design sends 860 bytes per machine per second: 0.69 Mbps for the fleet and about 0.4 TB a year in the lake instead of 378 TB.

## Slide 9: A cloud bill has four blocks, and three ways of charging
STEP 3 · PRICE
Block | AWS | Azure | GCP
1 Ingestion | IoT Core: $1.05 per million messages (5 KB units) + rules | IoT Hub: fixed units, S2 = $350/month for 6 M messages/day (4 KB units) | Pub/Sub: $40 per TiB + 3 broker VMs ($60 each, assumed)
2 Stream | Kinesis, 2 shards | Event Hubs, 2 TU | Dataflow, 1 worker (assumed)
3 Lake | S3 $0.025/GB-month | ADLS $0.020/GB-month | Cloud Storage $0.020/GB-month
4 PostgreSQL | RDS 2 vCPU + 128 GB | Flexible Server B2s | Cloud SQL 2 vCPU
Charges by | number of messages | fixed daily quota | bytes
Excluded: egress, support, discounts, GST, edge hardware, labour. Indicative, for comparing designs, not a quote.
Notes: Every cloud has the same four blocks: ingestion, streaming, lake, database. The key difference is the meter. AWS charges per message, Azure sells fixed units with a daily quota, and Google charges by bytes. That one fact explains every result that follows.

## Slide 10: Scenarios S0 to S3
STEP 3 · FOUR WAYS TO SEND THE SAME DATA
 | What is sent per machine per second | Message size | Messages a month
S0 | every reading as its own message (110 messages) | 125 B | 28.5 billion
S1 | 1 Hz + raw 100 Hz, batched into 1 message | 1,025 B | 259.2 million
S2 (ours) | 1 Hz + 42 edge features, batched | 860 B | 259.2 million
S3 | 1 Hz + raw 2 kHz × 3 axes, batched | 42,376 B | 259.2 million
Messages = 100 machines × 2,592,000 s × 1 = 259.2 M · Stored GB = GB a month × 12 months ÷ compression
Notes: Same factory, four ways of sending. S0 sends every reading as its own message: 28.5 billion a month. S1 to S3 batch one message per machine per second: 259.2 million. S2, our design, uses edge features: 860 bytes. We keep 12 months in the lake, compressed.

## Slide 11: ₹33k to ₹80k a month, and storage is under ₹1,000
STEP 3 · WORKED EXAMPLE, OUR DESIGN (S2)
Block (₹/month) | AWS | Azure | GCP
Ingestion | 33,535 | 66,300 | 17,817
Stream | 2,841 | 4,779 | 4,774
Lake | 918 | 734 | 734
PostgreSQL | 5,827 | 8,271 | 9,603
Total | 43,121 | 80,085 | 32,928
AWS ingestion: 259.2 M × $1.05 + 259.2 M × $0.316 = $354 → ₹33,535
Azure: 259.2 M ÷ 30 = 8.64 M/day → 2 × S2 units × $350 = $700 → ₹66,300 (83 % of Azure's bill)
GCP: 0.203 TiB × $40 = $8 + 3 VMs × $60 = $188 → ₹17,817
Lake: 222.9 GB × 12 ÷ 6.9 = 388 GB × $0.020–0.025 = ₹734–918
In IoT you pay for moving data, not for keeping it.
Notes: Here is our design priced. AWS: 259 million messages at $1.05 a million plus rules, about ₹33.5k. Azure: 8.64 million a day needs two S2 units, $700, which is 83 percent of its bill. GCP charges bytes: only $8 of data, the rest is broker VMs. Storage, what people worry about, is under ₹1,000 a month everywhere. Totals: GCP ₹33k, AWS ₹43k, Azure ₹80k.

## Slide 12: Design choices move the bill more than the cloud does
STEP 3 · ALL RESULTS
₹ per month | AWS | Azure | GCP
S0 one message per reading | 29.9 lakh | 14.3 lakh | 55k
S1 raw 100 Hz, batched | 43k | 80k | 33k
S2 edge features (ours) | 43k | 80k | 33k
S3 raw 2 kHz | 2.85 lakh | 3.94 lakh | 1.19 lakh
69×
cheaper on AWS just by batching (S0 → S1)
₹2.4–3.1 lakh
saved a month by edge features at the real 2 kHz rate (S3 − S2, AWS/Azure)
≈ 1.6 %
Azure's ₹9.6 lakh a year vs ₹5.84 crore estimated benefit
Notes: Three lessons. Batching alone makes AWS 69 times cheaper: ₹30 lakh down to ₹43k, a few lines of edge code. At the real 2 kHz rate, edge features save ₹2.4 to 3.1 lakh a month. And the difference between clouds is about 1 to 2 percent of the expected benefit, which is why cost is only 13 percent of our decision weight. GCP looks cheap in S0 because it bills bytes; its real figure would be higher because of per-request minimums.

## Slide 13: Lake, warehouse, lakehouse: where the cost comes from
STORAGE CHOICE
₹7.2 lakh
a month to keep a year of raw 2 kHz in a lake (378 TB × $0.020)
₹2 lakh
for ONE full BigQuery scan of that raw data (344 TiB × $6.25)
≈ ₹1,000
a month for a year of edge features (0.53 TB)
₹0
our live prototype: BigQuery sandbox, 10 tables, ~1.27 M rows
Lake and warehouse storage cost about the same per GB ($0.020–0.025).
A warehouse's real cost is compute: BigQuery charges $6.25 per TiB scanned.
The edge is what makes the warehouse affordable.
Notes: Storage per GB is similar in a lake and a warehouse. The warehouse cost is scanning: one query over a year of raw vibration would cost ₹2 lakh. With edge features the whole year is about ₹1,000 a month, and our live prototype runs free on the BigQuery sandbox.

## Slide 14: Weighted decision matrix: cost is 13 of 100 points
STEP 4 · DECIDE
Criterion | Weight | AWS | Azure | GCP
Industrial IoT / OT connectivity | 15 | 4 | 5 | 2
Indicative cost | 13 | 4 | 2 | 5
Edge and offline | 12 | 4 | 4 | 2
Security and India residency | 12 | 4 | 4 | 3
Storage and data lake | 10 | 4 | 5 | 4
Stream and analytics | 10 | 3 | 5 | 4
AI / ML | 10 | 5 | 4 | 5
Integration (ERP, M365, OPC UA) | 8 | 3 | 5 | 4
Scalability | 5 | 5 | 5 | 5
Ease and skills | 5 | 3 | 4 | 3
Weighted total | 100 | 3.92 | 4.22 | 3.57
Total = Σ (weight × score) ÷ 100
Azure: 75 + 26 + 48 + 48 + 50 + 50 + 40 + 40 + 25 + 20 = 422 → 4.22
Cost score is computed: cheapest = 5, others = 5 × cheapest ÷ cost
AWS: 5 × 32,928 ÷ 43,121 = 3.8 → 4; Azure: 5 × 32,928 ÷ 80,085 = 2.1 → 2
Notes: Ten criteria, weights adding to 100, scores 1 to 5 with evidence. Machine connectivity carries the most weight because a factory platform lives or dies there. The cost score isn't opinion: it comes from the cost model, cheapest gets 5. Azure totals 422 points, 4.22; AWS 3.92; GCP 3.57.

## Slide 15: Azure wins unless cost is a third of the decision
STEP 4 · IS IT ROBUST?
35 %
cost weight needed before AWS overtakes Azure (we use 13 %)
88.7 %
of 10,000 Monte Carlo runs won by Azure (AWS 10.9 %, GCP 0.4 %)
5 of 6
weight profiles won by Azure; only cost-heavy picks AWS
Notes: Weights are judgement, so we tried to break the result. AWS only wins if cost gets 35 percent of the weight. We ran the matrix 10,000 times with random weights and scores shifted up to half a point: Azure won 89 percent. Our live demo runs on GCP BigQuery because that account was available, and the same SQL gave the same answers as PostgreSQL, so the design is portable.

## Slide 16: Process at the edge, batch the messages, then choose the cloud
THE TAKEAWAY
378 TB → 0.4 TB a year · ₹30 lakh → ₹43k a month by batching · cloud cost ≈ 1–2 % of the benefit · Azure recommended, 4.22
Notes: Raw vibration can't go to the cloud: it's 378 terabytes a year and fills the plant's line. Edge features cut it a thousand-fold, batching cuts the bill up to 69 times, and once that's done the cloud choice is about capability, not price. That's why we recommend Azure. Happy to take questions.